## Slide 1: Network Simulation using NS2
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
by K.Rasagnya

## Slide 2: Contents
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Introduction to Network
Data communication
Components of Data communication
Direction of Data
OSI Model
TCP/IP protocol suite
Introduction to Network Simulator and its architecture
Network in NS2
Basic Linux commands
Installation of NS2

## Slide 3: Contents
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Steps to create a wired network scenario ﬁle
Execution of simulation and analysis of network using awk files
Procedure for simulation and analysis
Writing a TCL script to create two nodes and links between nodes
Writing a TCL script to transmit data between nodes
Wired Network Trace file format and analysis of simulation using awk script
Adding colour, shape and labelling the node and adding colour to the data traffic

## Slide 4: Contents
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Writing a tcl script to label link and adding colour to the link
Writing a TCL script for UDP communication between sender & receiver
Performance evaluation of various Topologies
TCL script to simulate bottleneck network
Performance evaluation of Drop Tail and RED queue management schemes
Introduction and Installation of gnuplot and xgraph
TCL script to plot congestion for different sources and destinations

## Slide 5: Contents
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Plotting two or more files in one graph using gnuplot
Simulate to compare packet size and throughput
TCL script to simulate link state routing protocol
Steps to create a wireless network scenario ﬁle using DSDV
Performance Analysis of wireless network using awk files
Steps to create a wireless network scenario ﬁle using DSR
Tcl script to label, colour and marking the node in Wireless Networks

## Slide 6: Contents
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Performance evaluation of AODV Routing Protocol for Wireless Networks
Simulate to determine the performance with respect to different sources in Wireless Networks
Simulation and analysis of node movement in Wireless Networks
Tcl script to create traffic sessions for Wireless Networks using cbrgen
Tcl script to create mobility for Wireless Networks using setdest
Do’s and Don’ts in NS2

## Slide 7: Introduction
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Network :
  Network is a group of connected, communicating devices such as computers and printers etc.
Computer Network :
  It is a collection of various computing devices.
Need of Computer Network :
  A network is formed for resource sharing i.e., sharing available information to anyone on the network.

## Slide 8: Data Communication
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Sender
Receiver
Rules
Rules
Protocol
Protocol
Medium
Message

## Slide 9: Components of Data communication
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Message :
  It is the information(data) to be communicated.
  Popular forms of information include text, numbers, pictures, audio, video.
Sender :
  It is the device that sends the data message.
  It can be a computer, telephone, handset, video camera etc.
Receiver :
  It is the device that receives the message.

## Slide 10: Components of Data communication
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Transmission Medium :
  It is the physical path by which a message travels from sender to receiver.
  It can be wired or wireless.
  Examples : twisted coaxial cable, fibre optic cable, radio waves etc.
Protocol :
  It is set of rules that governs data communication.
  It represents an agreement between the communicating devices.
  The networking devices like computers should follow to transfer data efficiently.

## Slide 11: Components of Data communication
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
  A Protocol defines
    What is communicated
    How it is communicated
    When it is communicated
  Key elements of Protocol are
    Syntax
    Semantics
    Timings

## Slide 12: Components of Data communication
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
  Syntax :
    Refers to the structure or format of the data, meaning the order in which they are presented.
    Example :
      First 8 bits  Address of Sender
      Next 8 bits  Address of Receiver
      Rest of stream  Message

## Slide 13: Components of Data communication
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
  Syntax :
    The data order is also applied to the order of bits when they are stored or transmitted.
    Different computers may store data in different bit orders.
    When these computers communicated, this difference needs to be resolved.

## Slide 14: Components of Data communication
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
  Semantics :
    Refers to the meaning of each section of bits.
  Timings :
    Refers to 2 characteristics
      When data should be sent
      How fast it can be sent

## Slide 15: Direction of Data
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Communication between any two devices can be simplex, half-duplex, or full-duplex.
Simplex :
In simplex mode, the communication is unidirectional. Only one of the two devices on a link can transmit and the other can only receive.
keyboard
Monitor
Direction of data

## Slide 16: Direction of Data
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Keyboards and traditional monitors are examples of simplex devices. The keyboard can only introduce input and the monitor can only accept output.
The simplex mode can use the entire capacity of the channel to send data in one direction.
Half-duplex :
In half-duplex mode, each station can both transmit and receive, but not at the same time. When one device is sending, the other can only receive, and vice versa.

## Slide 17
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
System1
System2
Direction of data at time 1
Direction of data at time 2
Full-duplex :
In full-duplex mode (also called duplex), both stations can transmit and receive simultaneously.
System1
System2
Direction of data all the time

## Slide 18: OSI Model
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
When communication is not simple, we may divide the complex task of communication into several layers.
OSI model is used to have successful communication between computers or networks of different architectures
The OSI reference model describes how information from a software application in one computer moves through a network medium to a software application in another computer.
The model was developed by ISO and it is composed of seven layers each specifying a particular network function.
Each layer is a package of protocols.

## Slide 19: OSI Model
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Application
Presentation
Session
Transport
Network
Data Link
Physical
To translate, encrypt and compress data
To establish, manage and terminate sessions, authentication and authorization
To provide segmentation, flow control and error control
To provide logical addressing,
Routing and path determination
To organize bits into frame and to provide medium access control and error recovery
To transmit bits over a medium
and to provide mechanical and electrical specifications
Enables the users to access the network

## Slide 20: OSI Model
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Application Layer :
Enables the users to access the network.
This layer is used by network applications.
Network applications means computer applications that use internet like google chrome, Firefox etc.
These applications depend on application layer protocols to function.

## Slide 21: OSI Model
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
These Application Layer Protocols form the basis for various network services like file transfer, web surfing, sending emails etc.
  File transfer is done by FTP protocol.
  Web surfing is done with help of HTTP or HTTPS protocol.
  For emails, SMTP is used.
So, Application layer provides services for network applications with the help of protocols to perform user activities.

## Slide 22
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Presentation Layer :
It receives data from application layer.
Presentation layer performs 3 basic functions.
  Translation
  Compression
  Encryption / Decryption

## Slide 23
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Translation :
The data which is received from application layer is in the form of characters and numbers.
Presentation layer convert these characters and numbers to machine understandable (binary) language.
Example : Conversion of ASCII to Binary
DFGJC 10010

## Slide 24
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Data Compression :
Before the data is transmitted, Presentation layer reduces the number of bits that are used to represent the original data.
This bit reduction process is called “Data Compression”.
It reduces the amount of space used to store the original file.
As the size of the file is reduced, it can be received at the destination in very less time i.e., data transmission can be done faster.

## Slide 25
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Encryption / Decryption :
To maintain integrity of data, before transmission, “data is encrypted”.
Encryption enhances security of sensitive data.
Secure Socket Layer ( SSL ) is used in Presentation layer for encryption and decryption.
  At Sender side, data is Encrypted.
  At Receiver side, data is Decrypted.

## Slide 26
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Session Layer :
It helps in setting up and managing connections enabling sending and receiving of data, followed by termination of connections or sessions.
Just before a session or a connection is establishment with a server, server performs a function called “Authentication”.
After authenticating the user, “Authorization” is checked.
Thus the session layer helps in
  Session management
  Authentication
  Authorization

## Slide 27
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Transport Layer :
Transport layer controls reliability of communication through
  Segmentation
  Flow control
  Error control
Protocols of transport layer are
  Transmission Control Protocol (TCP)
  User Datagram Protocol (UDP)

## Slide 28
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Segmentation :
Data received from session layer is divided into small data units called segments.
Each segment contains a source and destinations Port Numbers and a Sequence Number.
Data
Data 1
Data 2
Data 3

## Slide 29
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Flow control :
It controls the amount of data being transmitted.
Server
Mobile
100 Mbps
50 Mbps
Server
Mobile
50 Mbps
50 Mbps

## Slide 30
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Error control :
Transport layer also helps in error control.
If some data does not arrive the destination, transport layer uses “Automatic Repeat Request” to retransmit the lost or corrupted data.
A group of bits called checksum is added to each segment by the transport layer to find out the received corrupted segment.

## Slide 31
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Network Layer :
Transport layer transmits segments to network layer.
Network Layer works for the transmission of received data segments from one computer to the other computer located in different network (internetworking).
Data units in the network layer are called “Packets”.
In Network Layer we have routers.

## Slide 32
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Functions of Network Layer :
Logical addressing :
  IP addressing done in Network Layer is called Logical addressing.
  IP address are assigned to ensure each data packet can reach the correct destination.
Packet
Segment | IP address (Sender) | IP address (Receiver)

## Slide 33
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Routing :
  It is the process of moving data packet from source to destination and it is based on the logical addressing.
Path determination :
  A computer can be connected to internet server or to a computer in number of ways.
  Choosing the best possible path for data deliver from source to destination is called Path determination.

## Slide 34
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Data Link Layer :
It receives data packets from Network layer.
Data Link Layer is embedded as software in NIC of a computer and provide means to transmit data from one computer to other computer via a local media ( copper wire, optical fibre, air ).

## Slide 35
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Functions of Data Link Layer :
Physical addressing :
  It allows upper layer of OSI model to access the media using technique called framing.
  MAC address of sender and receiver are added to data packet to form a frame.
Frame
MAC 1 | MAC 2 | Packet | Tail

## Slide 36
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Medium Access Control :
  The technique used to get the frame on and off the media is called Medium Access Control.
  If two or more devices connected to the same media and send data at the same time, then there will be a possibility of collision of two messages.
  To avoid these situations, DLL checks when the shared media is free. This is called CSMA ( Carrier Sense Multiple Access ).
Error Detection :
  Tail of each frame contains bits which are used to detect errors.

## Slide 37
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Physical Layer :
It receives data from Data Link layer which is a sequence of binary numbers.
Physical Layer converts these binary sequence into signals and transmits over local media .

## Slide 38: TCP/IP Protocol Suite
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Application
Transport
Network
Data Link
Physical
Developed from OSI model.
It is made up of five layers.
The first four layers provide physical standards, network interface, internetworking and transport functions.
The three topmost layers in the OSI model, however are represented in TCP/IP by a single layer called the application layer.

## Slide 39: What is NS2 ?
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Ns2 stands for Network Simulator version 2.
It is an open source simulator designed for research in computer networks.
Network Simulator is a software that predicts the behavior of computer network.
Setting up a network to do some real experiments is the best way for studying about computer networks.
However, setting a network is not easy and costly.
For this reason, a virtual network provided by network simulator is used for experiment in only one computer.

## Slide 40: What is NS2 ?
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
In simulator, the computer network is modeled. The network model describes
  the network (devices, links, application etc.)
  the events ( data transmission, packet error etc.).
Output results include performance metrics of network like sent packets, received packets, throughput, delay, packet drop etc.
Trace files are also available which describes the every event occurred in the simulation and are used for analysis.

## Slide 41: Reasons for Using NS-2
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
1. It does not require costly equipment.
2. Complex scenarios can be easily tested.
3. Results can be quickly obtained.
4. More ideas can be tested in a smaller time frame.
5. Controlled experimental conditions.

## Slide 42: Network simulation
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
It uses programming to represent devices.
Easy and can be easily verified.
It is a event driven simulator.
It provides support for
  simulation of TCP, UDP.
  Routing.
  Huge number of protocols ranging from wired to wireless networks.
  support the addition of new entities like agents, packet, application, queue, protocol, routing etc.
  Errors are being discovered and corrected.

## Slide 43: NS2 Architecture
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
Simulation objects
NS2 Shell Executable Command (ns)
Simulation
Objects
Simulation
Objects
TclCL
TCL
Simulation
Script
Simulation
Results
C++
OTcl
NAM
( Animation )
Trace file

## Slide 44: Network simulation
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
NS2 use Tcl language for creating simulation scenario ﬁle (for example, ns1.tcl).
ns1.tcl :
  It is the name of a tcl script file which defines the simulation scenario.
  Network topology, transmission time, using protocol etc... are deﬁned in scenario ﬁle.
If we execute this scenario ﬁle, the simulation results will be ns1.tr and ns1.nam ﬁle.
ns1.tr :
  all the information about communication is written in this ﬁle.
  This ﬁle is called as Trace ﬁle.
ns1.nam :
  Used to visualize the simulation.
  This ﬁle can be execute by Nam, an animation software.

## Slide 45: General work process of NS2
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in

## Slide 46: Network in NS2
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
FTP , CBR HTTP , SMTP | 
TCP | UDP
IP | 
Ethernet | 
FTP , CBR HTTP , SMTP | 
TCP | UDP
IP | 
Ethernet | 
IP
Ethernet
Sender
Receiver
cable
cable
Application
Transport
Network
Physical, Datalink
Router

## Slide 47: Network in NS2
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
The node (terminal, router) in real network have 4 layer using TCP/IP model.
Actually, forwarding node (router) have only 2 bottom layer.
Two bottom layers are ready automatically when a node setting up.
TCP or UDP in transport layer are shown as Agent. FTP, CBR are in application layers.
Realistic networks use cable for link between 2 nodes. In NS2, a link is use for connection. Each link has a queue which is similar to buﬀer in realistic network. Packets sent from node should be queuing in queue.

## Slide 48: Platforms to install NS2
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Linux operating system
  Ubuntu
  Fedora
  Linux mint
Windows

## Slide 49: Requirements of NS2
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
ns-allinone-2.35 software
NSG2.1 software
Gnuplot
Xgraph

## Slide 50: Basic Linux Commands
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
cp : copy files
rm : remove or delete files
make : to compile or recompile
gedit : editors (similar to notepad)
pwd : Present Working Directory.
passwd : to change the user password.
clear : to clear the screen.

## Slide 51: Basic Linux Commands
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
mkdir : to create a directory.
rmdir : to delete directory.
cd : to change the directory.
cd .. : previous directory
ls : to list the contents of current directory.
ls –l : long format of showing list of files.
chmod : changing the mode of the file.

## Slide 52: Long format of file
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
 | r | w | x | r | w | x | r | w | x
Owner
Group Users
Other Users
r : read
w : write
x : execute
- : File
d : Directory

## Slide 53: Long format of file
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
- | r | w | x | r | - | x | r | - | -
Owner
can
Read, write and execute the file
Group Users
can
Read and execute
the file
Other Users can only read file
Indicates File
Ex :

## Slide 54: Steps to create a wired network scenario ﬁle
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Declare Simulator
Create output ﬁles (tracing and animation file )
Setting Node
Setting Link between the nodes
Setting Agent
Setting Application
Setting time schedules for Simulation
Declare ﬁnish

## Slide 55: Steps to create a scenario ﬁle
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Declare Simulator :
  S should be capital letter in Simulator.
  Simulator is the name of the c++ class. We have to call this c++ class from the precompiled library.
  new is to create the instants of this simulator.
  set ns [new Simulator]

## Slide 56: Steps to create a scenario ﬁle
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Create output ﬁles :
Setting Node :
  set tracefile [open ns1.tr w]
  $ns trace-all $tracefile
  set namfile [open ns1.nam w]
  $ns namtrace-all $namfile
  set n0 [$ns node]
  set n1 [$ns node]

## Slide 57: Steps to create a scenario ﬁle
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Setting Link :
  In line 1, a duplex link between n0 and n1 is declared.
  The link between two nodes n0 and n1 has bandwidth 3Mbps and delay 5ms.
  DropTail is a waiting queue type.
  Line 2 sets positions of node and link for Nam.
  $ns duplex-link $n0 $n1 3Mb 5ms DropTail
  $ns duplex-link $n0 $n1 orient right-down

## Slide 58: Steps to create a scenario ﬁle
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Setting Agent :
UDP Agent :
  set udp [new Agent/UDP]
  $ns attach-agent $n0 $udp
  set null [new Agent/Null]
  $ns attach-agent $n1 $null
  $ns connect $udp $null
To use UDP in simulation, the sender sets the Agent as UDP Agent while the receiver sets to Null Agent.
Null Agents do nothing except receiving the packets.
In ﬁrst 4 lines, udp and null Agent are set for n0 and n1, respectively.
Line 5 declares the transmission between udp and null.

## Slide 59: Steps to create a scenario ﬁle
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Setting Agent :
TCP Agent :
  set tcp [new Agent/TCP]
  $ns attach-agent $n0 $tcp
  set sink [new Agent/TCPSink]
  $ns attach-agent $n1 $sink
  $ns connect $tcp $sink
To use TCP in simulation, the sender sets the Agent as TCP Agent while the receiver sets to TCPSink Agent.
When receiving a packet, TCPSink Agent will reply an acknowledgment packet (ACK).
In ﬁrst 4 lines, tcp and sink Agent are set for n0 and n1, respectively.
Line 5 declares the transmission between tcp and sink.

## Slide 60: Steps to create a scenario ﬁle
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Setting Application :
  UDP Agent uses CBR Application
  TCP Agent uses FTP Application.
  set cbr [new Application/Traffic/CBR] $cbr attach-agent $udp
  set ftp [new Application/FTP]
  $ftp attach-agent $tcp

## Slide 61: Steps to create a scenario ﬁle
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Setting time schedule for simulation :
  cbr transmits data from 1.0[sec] to 8.5[sec]
  ftp transmits data from 2.5[sec] to 8.0[sec]
  $ns at 1.0 "$cbr start"
  $ns at 2.5 "$ftp start“
  $ns at 8.0 "$ftp stop"
  $ns at 8.5 "$cbr stop"

## Slide 62: Steps to create a scenario ﬁle
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Declare ﬁnish : Simulation will stop at 10 sec
  $ns at 10.0 "finish"
  proc finish {} {
  global ns tracefile namfile
  $ns flush-trace
  close $tracefile
  close $namfile
  exit 0
  }
  $ns run

## Slide 63: Execution of Simulation
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
  By executing below command line, simulation will be started.
  After the simulation, Nam will be started and shows the animation of simulation.
  Command for opening nam file directly
  ns ns1.tcl
  nam ns1.nam

## Slide 64: Analysis of Simulation
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
  AWK is a high level programming language which is used to process the text files.
  Its name is derived from the family names of its authors
    A : Alfred Aho
    W : Peter Weinberger
    K : Brian Kernighan
  AWK scripts are very good in processing the data column wise from long trace files which we get from NS2.

## Slide 65: Analysis of Simulation
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
  It contains mainly three parts
    Begin
    Content
    End
  We have to run the AWK scripts using the following command
  awk –f wired.awk ns1.tr

## Slide 66: Procedure for simulation and analysis
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
1. Open terminal and go to the directory where the jar file is present.
2. After going to the directory to open the jar file.
Type the command:
java –jar NSG2.1.jar
Where, NSG2.jar is the jar file name.
3. In scenario select new wired or wireless scenario. Place nodes wherever necessary and link the nodes.
4. Attach tcp or udp to source node and tcp sink or null to destination node in the Agent tab.
5. Connect to source and destination i.e., tcp and tcpsink or udp and null.
6. Attach ftp or cbr to source in the Application tab.

## Slide 67
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
7. In parameters give nam and trace files name in simulation tab. Select routing protocol in wireless tab.
8. Click on tcl to get tcl code. Save the file as <filename>.tcl
9. Go to the tcl file directory in terminal and execute file by command
ns <filename>.tcl
10. After executing tcl file, NAM file and trace file are generated.
11. The simulation can be seen in the network animator.
12. Analyze the files using awk files, to calculate the parameter values type the following command
awk –f <awk filename >.awk <trace filename >.tr

## Slide 68: Transport Layer Protocols
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
A Transport Layer has several responsibilities
  1. To create a process to process communication.
  2. To provide error and flow control mechanisms.
A Transport Layer has two important protocols.
1. User Datagram Protocol ( UDP )
2. Transmission Control Protocol ( TCP )

## Slide 69
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
User Datagram Protocol ( UDP )
It is a connectionless, unreliable transport protocol. It provides process to process communication.
There is no flow control mechanism and there is no acknowledgement for received packets.
UDP, however does provide error control to some extent. If UDP detects an error in the received packets, it silently drops it.
UDP is a very simple protocol using a minimum overhead. So if a process wants to send a small message and does not care much about reliability, it can use UDP.

## Slide 70
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Transmission Control Protocol ( TCP )
1. It is a connection oriented, reliable transport protocol. It performs all tasks required by transport layer.
2. TCP is responsible for delivery of the message to the appropriate application program. TCP groups
number of bytes into a packet called a segment.
3. TCP provide flow control and error control.
4. Error detection in TCP is achieved through the use of 3 simple tools
  Checksum: to check corrupted segments.
  Acknowledge: uses to confirm the receipt of those segments that have reached the destination.
5. Error correction is very simple, if a segment is corrupted or lost, the segment will be retransmitted.

## Slide 71
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Data Transmission using TCP or UDP

## Slide 72
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Acknowledgements
Acknowledgements in TCP

## Slide 73: Wired Network Trace file format
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Event :
First character in trace file represent type of event, i.e. packet dropped, received, added to queue.
Time :
Second field in trace file represent time in second at which event occurred.
Event | Time | From Node | To Node | Pkt Type | Pkt Size | Flags | Flow id | Src Addr | Dst Addr | Seq Num | Pkt Id
+ | An enqueue operation occurred on the device queue
- | A dequeue operation occurred on the device queue
d | A packet was dropped, typically because the queue was full
r | A packet was received by the net device

## Slide 74: Wired Network Trace file format
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
From and to Node :
Third and fourth field in trace file specify and sender and receiver of current packet.
Packet Type :
Fifth field in trace file represent type of packet. It can be tcp, ack, cbr, etc., depends on the application attached.
Packet size :
Sixth field show size of packet in bytes.
Packet type | Meaning
Tcp | Tcp packet
cbr | Cbr traffic packet
Ack | Acknowledge packet
Aodv | Aodv packet

## Slide 75
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Flow id :
This field is used to specify the data flow colour for the NAM display.
Source and Destination address :
Source and destination address is specifier in format of "addr.port". Port is also specified with node address.
Sequence number :
In ns2 agent can attach sequence number with packets. This field is used only when agent attach sequence number to packets.
Packet id :
Every packet has a unique identifier. Every time a new packet is generated, assigned a unique id to it.

## Slide 76: QOS Parameters Formula
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Throughput : Received Bytes *8
Simulation Time
Total Delay : Time delay of all received packets
Average Delay : Total Delay
Received Packets

## Slide 77: QOS Parameters Formula
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Packet drop : Number of dropped packets
Packet Drop Ratio : Dropped Packets * 100
Sent Packets
Packet Delivery Ratio : Received Packets * 100
Sent Packets

## Slide 78: QOS Parameters Formula
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Average Energy Consumed : Total Energy Consumed
Number of Nodes
Average Remaining Energy : Initial Energy – Average Energy Consumed
Control Overhead : Total Number of Routing Packets
Total Number of Data Packets

## Slide 79: Color definition for different traffic flow
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
1. After creating a ns Simulator, include these two lines
$ns color 1 Red ;
$ns color 2 Blue ;
2. In Agents Definition, after adding agents include below lines
$tcp0 set fid_ 1
$udp1 set fid_ 2

## Slide 80: Color, shape and labelling nodes
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
1. To change Color and shape of nodes
$n0 shape box
$n0 color purple
2. To label the node
$ns at 0.0 "$n0 label S1"
$ns at 0.0 "$n2 label S2“
( or )
$n4 label ”D1”
$n5 label ”D2”

## Slide 81: Color and labelling links
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
1. To change Color of links
$ns duplex-link-op $n0 $n1 color “green”
$ns duplex-link-op $n1 $n2 color “red”
2. To label the links
$ns duplex-link-op $n0 $n1 label “L1”
$ns duplex-link-op $n1 $n2 label “L2”

## Slide 82
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Network Topologies
Topology :
  Graphical Representation of the relationship of all the links and linking devices (nodes) to one another.
  It is two types
    Physical Topology
    Logical Topology

## Slide 83
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Network Topologies
Physical Topology :
  It describes the way computers connect with the help of cables.
cable

## Slide 84
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Network Topologies
Logical Topology :
  It describes the way data flows from one computer to another within a computer network.
Data

## Slide 85
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Network Topologies
Network topology refers to the way in which the devices are interconnected.
The most common computer network used to interconnect physically distributed computers is “Local Area Network”.
It is five types
    1. Star 2. Mesh
    3. Ring 4. Bus
    5. Hybrid

## Slide 86
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Star Topology :
In this topology computers connect to a central device, a switch or a hub with point to point communication links.
point to point connection means that there is dedicated link (cable) between the two devices, other devices cannot use it.
In this topology, if one computer wants to send data frame to another, first it should be sent to the central device.

## Slide 87
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Star Topology :
Then the central device either broadcast or unicast the received data frame towards the destination computer based on the type of central device used.
Broadcast : It means transmission of data to all connected devices.
unicast : It means transmission of data to the target device only.

## Slide 88
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Hub :
If the central device is hub, it broadcast the received data to all the connected computers.
Hub is a multiport repeater.
The frame has a destination MAC address which is unique to every computer present in a network.

## Slide 89
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Hub :
So only target computer accepts the frame others reject it.
Since a hub broadcasts the received data, so it increases unnecessary data traffic in the network.
To overcome this limitation, a switch is used as a central device.

## Slide 90
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Switch :
A switch stores the MAC address of the devices connected to its ports.
Switch knows the device with MAC address is connected to which port, so the switch forwards the received data frame to that port only.
Instead of broadcasting, switch unicast the frame.

## Slide 91
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Mesh Topology :
In this topology, each device is connected to all other device in the network.
Each device has a point to point connection with every other

## Slide 92
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Ring Topology :
It is a network configuration in which device connection create a circular direct path.
Each network device is connected to two other devices like point on a circle.

## Slide 93
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Bus Topology :
In bus topology there is a main cable and all the devices are connected to this main cable through drop lines.
Since all the data is transmitted over the main cable, there is a limit of drop lines and the distance a main cable can have.

## Slide 94
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Network Topologies

## Slide 95: LAN setup in ns2
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
  To make a LAN connection between nodes n1, n2, n3, n4 the following line should be added in the tcl script
  set lan [$ns newLan “$n1 $n2 $n3 $n4” 0.5Mb 30ms LL Queue/DropTail MAC/802_3 channel]

## Slide 96
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
rt model
It defines a model to be applied to the nodes and links in the topology.
If only one node is specified, it is assumed that the node will fail.
This is modelled by making the links incident on the node fail.
  $ns rtmodel-at 1.0 down $n(1)
  $ns rtmodel-at 2.5 up $n(1)
  $ns rtmodel-at <time> <up/down> <node>

## Slide 97
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
rt model
If two nodes are specified, then it is assumed that the two nodes are adjacent to each other and the model is applied to the link incident on the two nodes.
  $ns rtmodel-at 1.0 up $n(1) $n(2)
  $ns rtmodel-at 2.0 down $n(1) $n(2)

## Slide 98: Queue Management Schemes
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Performance of TCP based applications critically depends on the choice of Queue Management (Q.M) in the network links.
Queue Management is defined as the algorithm that manage the length of the packet queues by dropping packets when necessary.
From the point of packet dropping, Queue management can be classified into 2 types
  1. Passive Q.M : Packet drop occurs only when the buffer gets full
  Ex: Drop Tail.
  2. Active Q.M : Employs preventive packet drops. It provides implicit feedback mechanism to
  notify senders of the onset of congestion. Arriving packets are randomly dropped.
  Ex: RED

## Slide 99
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Drop Tail :
  1. Drops packets from the tail of the queue.
  2. Once buffer gets full, all arriving packets are discarded.
  3. Packets already in the queue are not affected.
Random Early Detection :
  1. RED accepts all packets until the queue reaches minth, after
  which it drops a packet with a linear probability distribution
  function.
  2. When the queue length reaches maxth all packets are dropped
  with probability of one.

## Slide 100: GNU plot
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
It is the most widely used open source program for plotting and visualizing data.
It is used to plot highly polished graphs for presentations and publications.
Gnuplot reads data from simple text files, with the data arranged in columns.
To plot a data file takes only a single command “plot”

## Slide 101: GNU plot
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
      plot “tcp1.plot”
      plot “tcp1.plot” using 1:2 with lines title “tcpcong” lw 2
The plot command requires the name of the data file in quotes
The rest of the command line specifies which columns to use for the plot and in which way to represent the data.

## Slide 102: GNU plot
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Gnuplot handles most of things by itself :
  It sizes the graph and selects the most interesting plot range.
  It draws the border.
  It draws the tick marks and their labels.
All these details can be customized.

## Slide 103: Steps for installation of gnuplot
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
1. Gnuplot is used to plot the results, to install gnuplot open terminal and type
2. Command to plot the results using gnuplot, open terminal and type
( or )
  cd press enter
  sudo apt install gnuplot
  gnuplot filename
  gnuplot
  plot “filename”

## Slide 104: Steps for installation of xgraph
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
1. If xgraph is not working download the other xgraph from the given link
http://www.xgraph.org/linux/index.html
2. Now extract the downloaded file on to Desktop and open terminal and type
xgraph it will display the xgraph.
3. If xgraph does not open, then open terminal and type the following commands
cd Desktop/
sudo cp xgraph /usr/local/bin/

## Slide 105: Steps for installation of xgraph
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in

## Slide 106: Node Movement
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
To generate movement setdest command is used.
  Ex: $ns at 1 " $n0 setdest 616 609 50 "

## Slide 107: Routing Protocols
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Adhoc wireless network consists of a set of nodes(hosts) that are connected by wireless links.
Routing protocols are used to find the path between source and destination for data transmission.
Types of Routing protocols
  DSR
  AODV
  DSDV

## Slide 108: Dynamic Source Routing(DSR) Protocol
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
DSR is an on-demand protocol designed to restrict the bandwidth consumed by control packets in ad hoc wireless networks by eliminating the periodic table-update messages required in the table-driven approach.
This protocol is truly based on source routing whereby all the routing information is maintained (continually updated) at mobile nodes.
It has only two major phases.
  Route Discovery
  Route Maintenance.
Consider a source node that does not have a route to the destination. When it has data packets to be sent to that destination, it initiates a Route Request packet. This Route Request is flooded throughout the network.

## Slide 109: Dynamic Source Routing(DSR) Protocol
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Each node, upon receiving a Route Request packet, rebroadcasts the packet to its neighbors if it has not forwarded it already, provided that the node is not the destination node and that the packet’s time to live(TTL) counter has not been exceeded.
Each Route Request carries a sequence number generated by the source node and the path it has traversed. A node, upon receiving a Route Request packet, checks the sequence number on the packet before forwarding it. The packet is forwarded only if it is not a duplicate Route Request.
The sequence number on the packet is used to prevent loop formations and to avoid multiple transmissions of the same Route Request by an intermediate node that receives it through multiple paths.
Thus, all nodes except the destination forward a Route Request packet during the route construction phase.

## Slide 110: Dynamic Source Routing(DSR) Protocol
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
A destination node, after receiving the first Route Request packet, replies to the source node through the reverse path the Route Request packet had traversed.
Advantages:
  This protocol uses a reactive approach which eliminates the need to periodically flood the network with table update messages which are required in a table-driven approach.
  In a reactive (on-demand) approach such as this, a route is established only when it is required and hence the need to find routes to all other nodes in the network as required by the table-driven approach is eliminated.
  The intermediate nodes also utilize the route cache information efficiently to reduce the control overhead.

## Slide 111: Dynamic Source Routing(DSR) Protocol
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Disadvantages:
  The disadvantage of this protocol is that the route maintenance mechanism does not locally repair a broken link.
  The connection setup delay is higher than in table-driven protocols.
  Even though the protocol performs well in static and low-mobility environments, the performance degrades rapidly with increasing mobility.
  Also, considerable routing overhead is involved due to the source-routing mechanism employed in DSR. This routing overhead is directly proportional to the path length.

## Slide 112: Ad hoc On-Demand Distance Vector(AODV) Routing Protocol
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
The AODV routing protocol is an on-demand routing protocol; all routes are discovered only when needed, and are maintained only as long as they are being used.
Routes are discovered through a route discovery cycle, whereby the network nodes are queried in search of a route to the destination node.
In AODV, if source node want to transmit data to the destination node, then source node broadcast route request packets(RREQ) to the neighboring nodes, if the neighboring nodes have path to destination node, again these nodes broadcast RREQ packets to their neighboring nodes.
If a node have a route to the destination, that route is reported back to the source node.

## Slide 113: Ad hoc On-Demand Distance Vector(AODV) Routing Protocol
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
If any link between nodes breaks in the selected route, the intermediate nodes both informs the end nodes about the path break by sending route reply packet with hop count as infinity(∞).
Advantages : Establish on demand, Destination sequences are used to find the latest path to destination connection setup delay is less in network.
Disadvantages : Intermediate node can lead to inconsistent route, Beacon-base, Heavy control overhead and more energy consumption it there is a path break.
On demand routing protocols have three types of control messages for route maintenance Route Requests(RREQs), Route Replies(RREPs), Route Errors(RERRs) .

## Slide 114: Ad hoc On-Demand Multipath Distance Vector(AOMDV) Routing Protocol
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
The AOMDV routing protocol is expanded to AODV protocol where the source node keeps several different routes from source to destination.
AOMDV routing protocol maintain multiple paths between the source and the destination in a single route discovery.
So, a new route discovery is needed only when all these paths fail.
The routing protocol has two mechanisms, route discovery and route maintenance.

## Slide 115
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Route Discovery
The route discovery process is similar to which used in AODV. It is started by RREQ when source node have some data for sending to the specific destination node.

## Slide 116
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Route Maintenance
When a link is broken due to the change of the network topology, intermediate nodes inform the route valid, by sending a RERR packet to the source node, as in the AODV protocol.
In this case, it uses alternative paths for transmitting remaining data packets.
If a corresponding RREP has not been received within the time, the entry is deleted. The routing table entry is modified for the maintenance of the multiple entries and multiple loop-free paths.

## Slide 117
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Represents Data packet transmission using alternate path from intermediate node after path break.

## Slide 118: Wireless Trace File format
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in

## Slide 119
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Example: s 0.032821055 _1_ RTR --- 0 message 32 [0 0 0 0] ------- [1:255 -1:255 32 0]
  It represent packet is sent at time .032821055 second by node 1.
  RTR represent that this packet is routing packet.
  Next three dashes are for flags.
  Sequence number of packet is 0. Type of packet is message.
  Size of this packet is 32 bytes.
  [0 0 0 0] first zero in bracket represent packet duration in mac layer header, second 0 is for mac address for destination, third zero for mac address for source and fourth zero for mac type of the packet body.
  Next dashes "-------" are flags, one of the flags is used for energy information of node.
  [1:255 -1:255 32 0] source node ip and port are 1 and 255 respectively, destination ip and port are -1 and 255.
  -1 is for broadcast address, next field 32 is tt1 field in ip header.

## Slide 120: Steps to create a wireless network scenario ﬁle
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Initialize variables
Create simulator objects
Create tracing and animation file
Create Topography
Create GOD
Create nodes
Create channel
Position of the nodes
Creation of agents and applications
Finish procedure

## Slide 121: Do's and Don'ts
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Do's :
  Vary only one parameter at a time.
  Consider the optimal simulation time to judge the protocol.
  According to our application and need, we have to consider the parameters.
  While comparing between two protocols, keep all the parameters same except routing protocol.

## Slide 122: Do's and Don'ts
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in
Don’ts :
  Never compare two different layer protocols.
  Don’t change multiple parameters for both the protocols.
  Don’t change the mobility files of the both the protocols.

## Slide 123: Thank you
EDUCATION
EMPLOYABILITY
ENTREPRENEURSHIP
www.task.telangana.gov.in